## Slide 1
SUNRISE OPEN CHALLENGE HACKATHON
PROBLEM STATEMENT : Drinking water
TEAM NAME : Aashman
TEAM MEMBERS : Brahadesh S B
Pooja Ragavi S
Anand Krishnan K
Lalith Kumar S
Hari Hara Bramma V

## Slide 2
OBJECTIVES
To remove the major contaminants (F, Cr and As) which cause kidney and other diseases before supplying the water to consumers from corporation.
To detect those contaminants by using separate reagents for F and Cr, then atomic absorption spectroscopy or Arsenic detection meter for As.
To filter the concern contaminants in water the filters like Ion exchange process, Activated carbon filtration and Sand based filters are used for F, Cr and As respectively. The flow of water is controlled by Solenoid tube valve.

## Slide 3
INTRODUCTION
We analyzed that Fluorine (0.1 to 8.8 mg/l at AP) is at alarm rate and also As and Cr.
Characteristics | Permissible limit
F | 1.0 mg/l
Cr | 0.05 mg/l
As | 0.05 mg/l
Characteristics | Permissible limit
Ca | 200 mg/l
Mg | 100 mg/l
Zn | 5 mg/l
Apparently the World Health Organization says that water with a TDS (total dissolved solids) of 1,000 PPM is “acceptable” and under 600 PPM is “good.”
Essential Constituents needed in Drinking water
Contaminants at higher level

## Slide 4
WORKING PROCESS
Fluoride detection
By adding the 1 ml of reagent in sample water. The Fluoride contained solution will remain colorless which indicates that Fluoride at higher level.
Chromium detection
By adding some drops of Cr reagents in sample water. The Chromium contained solution turns into dark which indicates that Chromium at higher level.
Arsenic detection
Arsenic level at water can be detected by using Arsenic detection meter or Atomic Absorption Spectrometer.
DETECTION
Fluoride detection

## Slide 5
F
As
Cr
F
Cr
As
Solenoid tube valves
Detection
Completely treated water
Completely treated water
Working model flow path
Ion exchange process
Activated carbon filter
Sand based filter
Coarse sand
Iron filings
Fine sand
F reagents
Cr reagents
AAS or Detection meter

## Slide 6
WORKING PROCESS
FILTRATION
After detecting the contaminants the concern path for filtration is manually chosen according to contaminants probability.
Fluoride filtration
Ion exchange process using Ion exchange resins.
Resins inside the filter exchange the ions to filter the Fluorine.
It exerts only 4% to 8% of waste water.
Generally it can filters 178 liters/kg of resin. Further we need to regenerate the resins by adding some acid and basic agents.
Lifetime is about 4 – 10 years according to level of contaminants.
It doesn’t remove Pathogens.

## Slide 7
F
As
Cr
F
Cr
As
Solenoid tube valves
Detection
Completely treated water
Completely treated water
Working model flow path
Filtration
Filtration
Filtration
Coarse sand
Iron filings
Fine sand

## Slide 8
FILTRATION
Chromium filtration
The filtration is done by using Activated carbon filters.
Activated carbon present inside of filters which effectively reduces the Chromium content.
Generally this type of filters improves taste, removes organic waste, Cl, Fe, Pb, Cd, Al, etc. and low maintenance cost.
Lifetime of filter is 2 – 5 years and replacement needed for every 200 liters of filtration.
It doesn’t remove viruses in water.

## Slide 9
F
As
Cr
F
Cr
As
Solenoid tube valves
Detection
Completely treated water
Completely treated water
Working model flow path
Filtration
Filtration
Filtration
Coarse sand
Iron filings
Fine sand

## Slide 10
FILTRATION
Arsenic filtration
It is sand based filters. Simply two bucket system.
The buckets are filled with 2 kg of coarse sand, 2 kg of fine sand, 3 kg of Iron filings, 1 kg of wood charcoal and some amount of brick chips.
It removes about 90 – 95 % of Arsenic.
Replacement of filtration should be done in the gap of 3 – 5 years.
It is simple, easy to install and low maintenance cost.

## Slide 11
F
As
Cr
F
Cr
As
Solenoid tube valves
Detection
Completely treated water
Completely treated water
Working model flow path
Filtration
Filtration
Filtration
Coarse sand
Iron filings
Fine sand

## Slide 12
EXISTING SOLUTION
Reverse osmosis
It is commonly used water filtration now a days.
It’s efficiency varies with cost of instrument. It varies from 10 to 1000 liters/hour.
But it completely reduce the traces of some most important essential salts (Ca, Mg and Zn).
Waste generation is higher in this system. It’s about 20 liters for every 1 liter filtered water.

## Slide 13
BUSINESS ESTIMATION
Ion exchanging process costs about Rs. 900 for purification of 1000 liters.
For Activating carbon filter it costs about Rs. 1700 for purification of 1000 liters.
Sand based filters costs about Rs. 2800 for lifetime of 3 – 5 years with maintenance.
Chart: 
| Ion exchange process | Activated carbon filtration | Sand based filter
Estimation (at Rs.)/ 1000 liters | 900 | 1700 | 2800

## Slide 14
EXISTING MODEL (RO) SOLUTION
Already explained that RO process sweeps out essential minerals needed for drinking water. It cause bone related diseases and Vitamin D deficiency diseases.
To overcome this we can add Ca, Mg and Zn minerals after the RO process artificially.
It’s applicable for small scale productions especially in household filters.
The normal household drinking water consumption is about 10 liters per days. It contains about 2g of Ca, 1g of Mg and 0.5g of Zn.
Through pellet we can add those minerals to RO treated water in the centrifugation tank.
But it reduces the sweet taste of water but healthy one to drink.